## Slide 1: Studies on Activation in the ATLAS cavern with MPX Detectors
Benedikt Bergmann
Institute of Experimental and Applied Physics, Czech Technical University in Prague, Czech Republic
On behalf of the ATLAS MPX detector group
Nedaa Asbah2 , Petr Beneš1 ,Bartoloměj Biskup1,
Jan Jakůbek1, Claude Leroy2, Stanislav Pospíšil1,
Jaroslav Šolc1, André Sopczak1, Vít Sopko1,
Paul Soueid2, Michal Suk1, Daniel Tureček1,
Zdeněk Vykydal1
1 IEAP CTU Prague, Czech Republic — 2 Université de Montréal, Canada
Dresden 07/03/2013
PRELIMINARY

## Slide 2: Overview
The ATLAS MPX-detector network
Method of studying the activation (example MPX01)
Overview over results for different detectors
Summary

## Slide 3: The ATLAS MPX detector network – Devices
Medipix 2 ASIC with 300µm Silicon layer
  256 x 256 pixel
  Pixel pitch 55 µm
Converter foils:
  6Li(n,α)3H: thermal neutrons
  recoiled protons below PE: fast neutrons
PE
PE + Al
Al
Uncovered
LiF

## Slide 4: The ATLAS MPX detector network – detected particle types
Efficiencies (for noncharged particles reduced by the conversion efficiency to detectable charged particles and geometry factors):
  Charged particles (above 8 keV): 100%
  X-rays (10 keV): ~80%
  Gamma-rays (above 1 MeV): ~0.1%
  Thermal neutrons (energy < 0.5 eV): ~1%
  Fast neutrons (MeV range): ~0.1%
Device lifetime:
  Expected to withstand up to 1013 n/cm2
  Before installation: tested up to 1.5x1012 n/cm2
  Current integral number of high energy transfer particles (HETP) impinging on MPX01: 2x1010 HETP/cm2

## Slide 5: The ATLAS MPX detector network – MPX positions
Side A
M1
M2
M3
M4
M5
M7
M8
M10
M11
M12
M13
M14
M15
M9
M6
Detector | X [m] | Y [m] | Z [m] | R [m]
MPX01 | -0.71 | 0.29 | 3.42 | 0.77
MPX02 | -2.23 | -1.12 | 3.42 | 2.50
MPX03 | -3.45 | -0.93 | 2.94 | 3.57
MPX13 | -2.21 | -1.02 | -3.42 | 2.44
Notes: Coordinates with respect to the beam line!

## Slide 6: Count rate at MPX01 site during and after collisions
Activation of surrounding material during collisions in the ATLAS detector
  Luminosity monitoring with MPX devices: Background contribution
  Dosimetric aspect: What is the time dependency of the ambient dose equivalent rate after the collisions?
pp-collision region
Notes: Collision period after collision period! Zoom into collision period then this plot and zoom ohter region!

## Slide 7: Count rates of the whole inves-tigated period (March – Dec 2012)
Especially to determine the components with long half lifes it is necessary to use as long period as possible

## Slide 8: Count rates at MPX01 site: decay period

## Slide 9: Describing the decay of activated products
Sum of radioactive decays of n isotopes:
Fit of sum of exponetial is an ill-conditioned problem
  Choose appropriate region without collisions (exclude collisions)
  Fit sum of two exponential decays
  Subtract faster decay component from data
  Repeat steps 2. and 3. until all data is fitted
Notes: Low luminuosity run excluded!

## Slide 10: Describing the decay of activated products
Sum of radioactive decays of n isotopes:
Fit of sum of exponetial is an ill-conditioned problem
  Choose appropriate region without collisions (exclude collisions)
  Fit sum of two exponential decays (with range 0 to estimated half life times 10)
  Subtract faster decay component from data
  Repeat steps 2. and 3. until all data is fitted

## Slide 11: Describing the decay of activated products
Sum of radioactive decays of n isotopes:
Fit of sum of exponetial is an ill-conditioned problem
  Choose appropriate region without collisions (exclude collisions)
  Fit sum of two exponential decays (with range estimated half life times 10)
  Subtract faster decay component from data
  Repeat steps 2. and 3. until all data is fitted

## Slide 12: Describing the decay of activated products
Sum of radioactive decays of n isotopes:
Fit of sum of exponetial is an ill-conditioned problem
  Choose appropriate region without collisions (exclude collisions)
  Fit sum of two exponential decays (with range estimated half life times 10)
  Subtract faster decay component from data
  Repeat steps 2. and 3. until all data is fitted

## Slide 13: Describing the decay of activated products
Sum of radioactive decays of n isotopes:
Fit of sum of exponetial is an ill-conditioned problem
  Choose appropriate region without collisions (exclude collisions)
  Fit sum of two exponential decays (with range estimated half life times 10)
  Subtract faster decay component from data
  Repeat steps 2. and 3. until all data is fitted

## Slide 14: Modelling one decay region with the fitted half lifes
components with longer half life present (have to be guessed for the further analysis)
Notes: Time to end -> time after collisions

## Slide 15: Equation to describe the whole set of data
Decay of atoms activated before i-th frame
Activation during i-th frame (valid only during collisions)
Mtot total count rate measured in the given MPX frame (normalized to unit time)
Mact count rate caused by all activation products created until the end of the given (i-th) MPX frame
 decay constant,  = ln(2)/T1/2; T1/2 is the half-life
t time period between the end of (i-1)-th frame and the end of i-th frame
Yk normalization constant, used to fit the growth/decay curve to the measured data
Deduced by Jaroslav Solc according laws of nuclear growth and decay
Notes: Define w_k; k_ and w_k determined from measurement

## Slide 16: Fitting the formula to the data
Measured count rates
Estimated activation count rate
Adapting half lifes from the fit and adding longer components
Guessing the yields

## Slide 17
Activation – MPX01 (example 1)
Measured count rates
Estimated activation count rate
Notes: Beam effects before collisions and unsuccessful fill!
Beam alignment problems and abort of fill!

## Slide 18
Activation – MPX01 (example 2)
Measured count rates
Estimated activation count rate
Notes: Beam effects before collisions and unsuccessful fill!
Beam alignment problems and abort of fill!

## Slide 19
Activation contribution to total count rate during collisions (MPX01)
Notes: Peaks -> Frames bigger gap? Resetting

## Slide 20
Activation contribution to total count rate during collisions (detail)
Notes: Peaks -> Frames bigger gap? Resetting

## Slide 21
Overview – Half lifes and yields
Activation component | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Half-life | 21.4 s | 2.7 min | 24 min | 3.9 h | 20 h | 7 d | 104 d | 350 d
Yield | 4.292E-03 | 2.413E-03 | 4.491E-04 | 4.860E-04 | 8.298E-04 | 6.472E-05 | 6.472E-05 | 0.000E+00
MPX01
Activation component | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Half-life | 21.4 s | 2.7 min | 24 min | 3.9 h | 21 h | 7 d | 32 d | 350 d
Yield | 3.816E-02 | 1.373E-02 | 2.396E-03 | 3.623E-03 | 2.667E-03 | 4.025E-04 | 1.421E-04 | 9.471E-05
Activation component | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Half-life | 21.4 s | 2.7 min | 24 min | 3.9 h | 22 h | 7 d | 32 d | 350 d
Yield | 3.816E-02 | 1.318E-02 | 2.941E-03 | 3.410E-03 | 4.091E-03 | 7.103E-04 | 3.315E-04 | 9.471E-05
Activation component | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Half-life | 21.4 s | 2.7 min | 24 min | 3.5 h | 19 h | 7 d | 111 d | 350 d
Yield | 3.816E-02 | 1.785E-02 | 2.832E-03 | 5.114E-03 | 3.576E-03 | 5.327E-04 | 1.894E-04 | 9.471E-05
MPX02
MPX03
MPX13
Notes: Data from the fit of MPX01 is also used as a starting point of the evaluation of the other detectors. The actual fit is done manually and similar half lifes were foud at the posotions of the different devices.
Sn = tin
Zn = zinc

## Slide 22: Summary
A method was described to estimate the count rates of activated products during and after collisions
  Estimate the background due to activation for the luminosity analysis
  To predict time dependence of count rates after the beam is off (using known conversion factors the ambient dose equivalent rate can be obtained)
Procedure was done for MPX01, MPX02, MPX03, MPX13 within the ATLAS-MPX detector network
  Similar half lifes were obtaines for all detectors

## Slide 23
Thank you for your attention!