## Slide 1
Hybrid Pixel Detectors
for Radiation Protection
Erik Fröjdh
Notes: ----- Meeting Notes (2/25/13 10:17) -----
ESR fellow Ardent project

## Slide 2: Outline
Medipix Collaboration
Hybrid pixel detectors
Signal formation
Mixed field response
Ongoing projects
  ATLAS-MPX
  ISS
Demonstration
Summary and Conclusions
Notes: ----- Meeting Notes (2/18/13 16:51) -----
Qestions are welcome during the whole talk

## Slide 3: Medipix Collaboration
Two active collaborations, Medipix2 and Medipix3
About 20 members both universities and research institutes.
Large variety of applications, from X-ray imaging to time of flight mass spectrometry and particle tracking.
ASIC design and coordination done at CERN

## Slide 4: Development Path
Medipix1
1um SCAMOS 64 by 64 pixels
Photon Counting Demonstrator (1997)
250nm IBM CMOS, 256 by 256 55um pixels
Full photon counting (2002)
130nm IBM CMOS, 256 by 256 55um pixels
Photon Counting, Spectroscopic, Charge Summing, Continuous Readout (2012)
Fast front end, Simultaneous ToT and ToA <20 Mcounts/cm2/s (2013)
Analogue (ToT) and Time Stamping (ToA) (2006)
Medipix2
Timepix
Medipix3RX
Timepix3
VELOpix
CLICPix
65nm, ~20um pixels
Future Hybrid Pixel Time tagging layer for the LCD project (20??)
4
Future LHCb readout – Data driven 40MHz ToT 12Gb/s per chip (2013) ~500 Mcounts/cm2/s
SmallPix
Fast front end, Simultaneous ToT and ToA (2013) 0-suppressed

## Slide 5: The Medipix2 Collaboration
Institut de Fisca d'Altes Energies, Barcelona, Spain
University of Cagliari and INFN Section thereof, Italy
CEA, Paris, France
CERN, Geneva, Switzerland,
Universitat Freiburg, Freiburg, Germany,
University of Glasgow, Scotland, UK
Universita' di Napoli and INFN Section thereof, Italy
NIKHEF, Amsterdam, The Netherlands
University of Pisa and INFN Section thereof, Italy
Laboratory of Molecular Biology, Cambridge, England, UK
Mid Sweden University Sundsvall, Sweden,
Czech Technical University, Prague, Czech Republic
ESRF, Grenoble, France
Academy of Sciences of the Czech Republic, Prague
Universität Erlangen-Nurnberg, Erlangen, Germany
University of California, Berkeley, USA
University of Houston, Texas, USA

## Slide 6: Hybrid Pixel Detectors

## Slide 7: Hybrid Pixel Detectors

## Slide 8: Timepix
Hybrid Pixel Detector
256x256 pixels
55um pixel pitch
Single Photon Processing
  Time-over-Threshold
  Time of arrival
  Photon Counting
Capable of operating in
both electron and hole
collection mode
~ 500 transistors / pixel

## Slide 9: Benefits of Single Photon Processing
Each sensor pixel has its own dedicated readout circuit
That circuit is sensitive only to the tiny electrical pulses generated by ionizing radiation in the sensor and not to other background noise
Because of this hybrid pixels deliver clean noise-free images
M. Campbell

## Slide 10: Cosmic Particles in the Alice Experiment

## Slide 11: Timepix
Compact system 15x60mm for the USB Lite read out including sensor
USB Connection to standard PC
Pixelman control software allowing scripting and plugins
Usb lite
Usb lite
Usb read out
Pictures courtesy of IEAP Prague

## Slide 12: Signal Formation
TH
time
amplitude
Moving charge induces a signal on the read out pad
Pulse height is proportional to the deposited energy
In order to detect a particle it has to interact with the sensor material and create electron-hole pairs

## Slide 13: Charge carrier simulation CdTe
By David Krapohl, Mid Sweden University

## Slide 14: Basic Particle Identification
Mixed radiation fields poses problems for dosimetric measurements.
An advantage of a pixelated detectors is that particles can be identified by their track shape.
This is based on the different ways the particles interact in the sensor.

## Slide 15: Basic Particle Identification
60keV Photons (241Am)
0.5MeV Electron (90Sr)
5.5MeV Alpha (241Am)
Pb ion with delta rays
Erik Heijne [2]

## Slide 16: Basic Particle Identification
Possible to categorize particles using track and energy information
Some types of particles are hard or impossible to separate
Additional convertors and filters improve the detection specificity
β- radiation or
Compton electrons?

## Slide 17: Neutron Detection
Neutron have no charge and are therefore not directly detectable by Coulomb interactions in the sensor.
Thermal neutrons are detected by the production of secondary radiation by neutron capture in a convertor layer
Ex. n + 6Li → α (2.05 MeV) + 3H (2.73 MeV)
Fast neutrons can be detected by elastic scattering in the sensor layer but for increased efficiency and specificity a hydrogen rich converter material as Poly ethylene is used.

## Slide 18: Neutron Detection
Medipix2MXR with different
convertors.
Work done by Z. Vykydal [1]

## Slide 19: Improved Neutron Detection
To separate heavy charged particles form neutron response test have been made with a multi layer detector.
Interactions registered in both layers
  Low LET signatures – minimum ionizing charge particles (muons, energetic electrons,...)
  High LET signatures – highly ionizing charged particles (~10 MeV protons,...)
Interactions registered in single layer only
  Low LET signatures – photon interactions in one of the sensitive layers
  High LET signatures – fast neutron interactions in polyethylene region or thermal neutron interactions in 6Li region
Work done by Z. Vykydal [1]
Example of particle identification using a two layer detector

## Slide 20: ATLAS-MPX Network
16 Medipix2MXR detectors with neutron convertors
Placed in the ATLAS experimental cavern
Installed in 2008 before the first LHC beam
Proposed upgrade to Timepix detectors
Work done by Z. Vykydal [1]

## Slide 21: ATLAS-MPX
Good agreement with beam luminosity and other instruments
Work done by Z. Vykydal [1]

## Slide 22: Radioactive Activation
Work done by Z. Vykydal [1]

## Slide 23: Timepix Detectors at ISS
5 Timepix Usb Lite detectors with 300um Si sensors are currently in operation at the ISS
Evaluated as an option for radiation field monitors and personal dosimeters
Mixed radiation field
Important to get the right quality factor for heavy ions

## Slide 24: Timepix Detectors at ISS

## Slide 25: Timepix Detectors at ISS
Heavy Ion fragment, Q factor ~ 25

## Slide 26: Demonstration

## Slide 27: Why use Hybrid Pixel Detectors for Mixed Field Radiation Measurements?
The chip is sensitive only to the tiny electrical pulses generated by ionizing radiation in the sensor and not to background noise
No background noise and multiple channels gives a high dynamic range (more then 9 orders of magnitude)
Energy information, track shape, different convertors and provides a high specificity in a mixed field
Flexible system, the use different sensor materials, filters, converters and stacking to tailor to a specific radiation field.

## Slide 28: Referenses
[1] Vykydal Z., Evaluation of Radiation Field Properties with Pixel Semiconductor Detectors Operating in Particle Tracking Mode, PhD. Thesis, Albert-Ludwigs-Universität Freiburg, 2012
[2] Heijne E., Measurements and possible identification of secondary GeV ions in the SPS H8 beam during the January 2013 LHC lead run, Presentation at the Medipix Meeting 30 January 2013

## Slide 29: Cluster Summing
662keV